## Slide 1: Open Land Agriculture Monitoring System

## Slide 2: Index
Sr. No. | Title | 
1 | User requirement | 
2 | Final requirement | 
3 | Block diagram | 
4 | Hardware specification | 
5 | Flow chart | 
6 | Images of project making | 
7 | Code simulation result | 
8 | Hardware and software integration result | 
9 | conclusion/summary | 

## Slide 3: User requirements
To Power on and power off Pump
  when water level in well goes low.
  when electricity comes in night, so pump should start automatically.
To check moisture in soil.
Weather rain alert(to warn farmer regardi ng rain, so farmer can spray or stop spraying pesticide on crops).
Automatic drip & Sprinkler irrigation.
To check if onion is spoil or not.
To monitor all farm using cctv cameras.
To monitor water, food & lifestyle of farm animals
Temperature monitoring System for crops and animals >> when temperature exceeds above normal level >> then fan starts in animal shed.
To check quality of air or gas for plants and animals.
To detect smoke or fire in farm.

## Slide 4: Final requirements
Soil moisture sensor.
Relay with LED or DC water pump.
Temperature sensor.

## Slide 5: Block diagram
PIC
Soil moisture sensor
LCD
Relay
Driver
Temperature sensor
Power supply

## Slide 6: Hardware Specification
Soil Moisture Sensor (SKU:SEN0114),(Company> DFROBOT)
1. Power supply: 3.3v or 5v
2. Output voltage signal: 0~4.2v
3. Current: 35mA
4. Pin definition:
Analog output(Blue wire)
GND(Black wire)
Power(Red wire)
5. Size: 60x20x5mm
6. Value range:
0 ~300 : dry soil
300~700 : humid soil
700~950 : in water

## Slide 7: Temperature sensor(DS18B20) / LM35:
Temperature Range: -55°C to +125°C (-67°F to +257°F).
Temperature Resolution: The sensor can provide temperature readings with a programmable resolution of 9 to 12 bits.
Accuracy: At 12-bit resolution, it has an accuracy of ±0.0625°C.
Operating Voltage: 3.0V to 5.5V.
Communication Protocol: The DS18B20 communicates using the 1-Wire communication protocol, which allows multiple DS18B20 sensors to be connected to a single data bus. Each sensor has a unique 64-bit serial code, enabling individual sensor identification on the bus.
Conversion Time: At 12-bit resolution, it typically takes around 750 milliseconds.
Temperature Alarms: It supports programmable high and low temperature alarm triggers, allowing the sensor to alert a microcontroller when the temperature crosses a specified threshold.
Data Output: Temperature data is output in digital format and can be read via the 1-Wire interface.
Package Type: The DS18B20 is available in various package types, including TO-92 (for through-hole mounting) and surface-mount packages, making it versatile for different applications.
Compatibility: The DS18B20 is widely supported by microcontrollers and single-board computers, such as Arduino, Raspberry Pi, and others, thanks to available libraries and code examples.

## Slide 8: LED
Super Bright Red
Voltage: 1.6v-1.9v
Typical: 1.8v
Current: 18mA
Intensity: 4,500mcd
Colour Freq: 620-628nm
Lens: Water Clear.

## Slide 9: Relay Module Specifications(5 V)
Normal voltage: 5V DC
Normal current: 70mA
Maximum load current: 10A/250V AC, 10A/30V DC
Maximum switch voltage: 250V AC, 30V DC
Operate time: ≤ 10ms
Release time: ≤ 5ms

## Slide 10: Flowchart:
Soil moisture sensor
Temperature sensor
Relay
LED
PIC Microcontroller
LCD output

## Slide 11: Images of component assembly

## Slide 12: Code simulation result images

## Slide 13: Hardware + Software integration result

## Slide 14: Conclusion